# BORE MAINTENANCE SHEET

| Station Name |
| --- |
| Unit Number | Well Name | Antecedent#1 Temperature at headworks (oC) | Maximum Shut in Pressure (kPa) | Recommended Shut in Test Time (min) #2 |

| COORDINATES | EASTING |  | NORTHING |  |
| --- | --- | --- | --- | --- |

| Insert photograph here (press Alt I P F then select photo from file and press OK) | caption |
| --- | --- |
|  | Headworks |
| Insert more rows (press Alt A I B) |  |

#1: Antecedent is the temperature on arrival, which can differ significantly from the groundwater temperature.

#2: Time that the well was shut in and pressure measurements taken.

INSPECTED BY: Date

| Components | Leakage | Condition good (G) / fair (F) / poor (P) | Comments / Action |
| --- | --- | --- | --- |
| MAIN VALVE Body Gland Spindle | Yes / No Yes / No N/A | G / F / P G / F / P G / F / P |  |
| CHECK OPERATION OF MAIN VALVE Note: After testing the operation of the main valve the gland may develop a small leak – retighten gland nuts on gland housing | Checked: Yes / No Operating: Yes / No |
| FLANGES Flange Bolts / Nuts Gaskets | Yes / No Yes / No Yes / No | G / F / P G / F / P G / F / P |  |
| DISTRIBUTION VALVES Glands Body Spindle Threads | Yes / No Yes / No N/A Yes / No | G / F / P G / F / P G / F / P G / F / P |  |
| PRESSURE TEST VALVE | Yes / No | G / F / P |  |
| DISTRIBUTION MANFOLD(S) | Yes / No | G / F / P |  |
| COOLING POND Isolation Valve Float Valve Liner Vegetation Dam Condition Fencing | Yes / No Yes / No Yes / No N/A Yes / No Yes / No | G / F / P G / F / P G / F / P N/A G / F / P G / F / P |  |
| PIPELINE Air relief Valve Tanks - Capital Float Valve Isolation Valve Overflow – fencing, erosion around base of tank Troughs – Capital – float valve | Yes / No Yes / No Yes / No Yes / No Yes / No Yes / No Yes / No | G / F / P G / F / P G / F / P G / F / P G / F / P G / F / P G / F / P |  |
| PACKER Pressure Stability of Headworks | Yes / No Yes / No | N/A G / F / P | Pressure reading kpa |
| DEGASSER Air Release Valve | Yes / No Yes / No | G / F / P G / F / P |  |

# Text boxes

Additional Comments: